## Slide 1: Computer Architecture Experiment
浙江大学计算机学院
陈文智、王总辉
{chenwz, zhwang}@zju.edu.cn
Topic 6. Pipelined CPU supporting
31 MIPS Instructions

## Slide 2: Outline
Experiment Purpose
Experiment Task
Basic Principle
Operating Procedures
Precaution
Checkpoints

## Slide 3: Experiment Purpose
Understand 31 MIPS instructions.
Master the design methods of pipelined CPU executing 31 MIPS instructions.
master methods of program verification of Pipelined CPU executing 31 MIPS instructions

## Slide 4: Experiment Task
Design of Pipelined CPU executing 31 MIPS instructions.
  Design datapath
  Design CPU Controller
Verify the Pipelined CPU with program and observe the execution of program

## Slide 5: Pipelined CPU supporting execution of 31 MIPS instructions
MIPS Instructions |  |  |  |  |  |  |  | 
Bit # | 31..26 | 25..21 | 20..16 | 15..11 | 10..6 | 5..0 | Operations | 
R-type | op | rs | rt | rd | sa | func |  | 
add | 000000 | rs | rt | rd | 00000 | 100000 | rd = rs + rt; with overflow | PC+=4
addu |  | rs | rt | rd | 00000 | 100001 | rd = rs + rt; without overflow | PC+=4
sub |  | rs | rt | rd | 00000 | 100010 | rd = rs - rt; with overflow | PC+=4
subu |  | rs | rt | rd | 00000 | 100011 | rd = rs - rt; without overflow | PC+=4
and |  | rs | rt | rd | 00000 | 100100 | rd = rs & rt; | PC+=4
or |  | rs | rt | rd | 00000 | 100101 | rd = rs ¦ rt; | PC+=4
xor |  | rs | rt | rd | 00000 | 100110 | rd = rs ^ rt; | PC+=4
nor |  | rs | rt | rd | 00000 | 100111 | rd = ~(rs ¦ rt); | PC+=4
slt |  | rs | rt | rd | 00000 | 101010 | if(rs < rt)rd = 1; else rd = 0; <(signed) | PC+=4
sltu |  | rs | rt | rd | 00000 | 101011 | if(rs < rt)rd = 1; else rd = 0; <(unsigned) | PC+=4
sll |  | 00000 | rt | rd | sa | 000000 | rd = rt << sa; | PC+=4
srl |  | 00000 | rt | rd | sa | 000010 | rd = rt >> sa (logical); | PC+=4
sra |  | 00000 | rt | rd | sa | 000011 | rd = rt >> sa (arithmetic); | PC+=4
sllv |  | rs | rt | rd | 00000 | 000100 | rd = rt << rs; | PC+=4
srlv |  | rs | rt | rd | 00000 | 000110 | rd = rt >> rs (logical); | PC+=4
srav |  | rs | rt | rd | 00000 | 000111 | rd = rt >> rs(arithmetic); | PC+=4
jr |  | rs | 00000 | 00000 | 00000 | 001000 |  | PC=rs

## Slide 6: Pipelined CPU supporting execution of 31 MIPS instructions
MIPS Instructions |  |  |  |  |  |  |  | 
Bit # | 31..26 | 25..21 | 20..16 | 15..11 | 10..6 | 5..0 | Operations | 
I-type | op | rs | rt | immediate |  |  |  | 
addi | 001000 | rs | rt | imm |  |  | rt = rs + (sign_extend)imm; with overflow | PC+=4
addiu | 001001 | rs | rt | imm |  |  | rt = rs + (sign_extend)imm;without overflow | PC+=4
andi | 001100 | rs | rt | imm |  |  | rt = rs & (zero_extend)imm; | PC+=4
ori | 001101 | rs | rt | imm |  |  | rt = rs ¦ (zero_extend)imm; | PC+=4
xori | 001110 | rs | rt | imm |  |  | rt = rs ^ (zero_extend)imm; | PC+=4
lui | 001111 | 00000 | rt | imm |  |  | rt = imm * 65536; | PC+=4
lw | 100011 | rs | rt | imm |  |  | rt = memory[rs + (sign_extend)imm]; | PC+=4
sw | 101011 | rs | rt | imm |  |  | memory[rs + (sign_extend)imm] <-- rt; | PC+=4
beq | 000100 | rs | rt | imm |  |  | if (rs == rt) PC+=4 + (sign_extend)imm <<2; | PC+=4
bne | 000101 | rs | rt | imm |  |  | if (rs != rt) PC+=4 + (sign_extend)imm <<2; | PC+=4
slti | 001010 | rs | rt | imm |  |  | if (rs < (sign_extend)imm) rt =1 else rt = 0; less than signed | PC+=4
sltiu | 001011 | rs | rt | imm |  |  | if (rs < (zero_extend)imm) rt =1 else rt = 0; less than unsigned | PC+=4
J-type | op | address |  |  |  |  |  | 
j | 000010 | address |  |  |  |  | PC = (PC+4)[31..28],address<<2 | 
jal | 000011 | address |  |  |  |  | PC = (PC+4)[31..28],address<<2 ; $31 = PC+4 | 

## Slide 7: Datapath of CPU supporting 31 MIPS Instr.

## Slide 8: signed and unsigned type
reg and wire are unsigned type in Default
Signed Type:
  reg signed
  wire signed
Type Conversion Function
  $signed()
  $unsiged()

## Slide 9: ALU
case (oper)
EXE_ALU_SLT: begin
if (sign)
result = $signed(a) < $signed(b);
else
result = ……
EXE_ALU_LUI: begin
result = ……
end
……
EXE_ALU_SR: begin
if (sign)
……
else
……
endcase

## Slide 10: Instr. Mem.(1)
0 : 3c010000; % (00) main: lui $1, 0 # address of data[0] %
1 : 34240050; % (04) ori $4, $1, 80 # address of data[0] %
2 : 0c00001b; % (08) call: jal sum # call function %
3 : 20050004; % (0c) dslot1: addi $5, $0, 4 # counter,DELYED SLOT(DS) %
4 : ac820000; % (10) return: sw $2, 0($4) # store result %
5 : 8c890000; % (14) lw $9, 0($4) # check sw %
6 : 01244022; % (18) sub $8, $9, $4 # sub: $8 <- $9 - $4 %
7 : 20050003; % (1c) addi $5, $0, 3 # counter %
8 : 20a5ffff; % (20) loop2: addi $5, $5, -1 # counter - 1 %
9 : 34a8ffff; % (24) ori $8, $5, 0xffff # zero-extend: 0000ffff %
A : 39085555; % (28) xori $8, $8, 0x5555 # zero-extend: 0000aaaa %
B : 2009ffff; % (2c) addi $9, $0, -1 # sign-extend: ffffffff %

## Slide 11: Instr. Mem.(2)
C : 312affff; % (30) andi $10, $9, 0xffff # zero-extend: 0000ffff %
D : 01493025; % (34) or $6, $10, $9 # or: ffffffff %
E : 01494026; % (38) xor $8, $10, $9 # xor: ffff0000 %
F : 01463824; % (3c) and $7, $10, $6 # and: 0000ffff %
10 : 10a00003; % (40) beq $5, $0, shift # if $5 = 0, goto shift %
11 : 00000000; % (44) dslot2: nop # DS %
12 : 08000008; % (48) j loop2 # jump loop2 %
13 : 00000000; % (4c) dslot3: nop # DS %
14 : 2005ffff; % (50) shift: addi $5, $0, -1 # $5 = ffffffff %
15 : 000543c0; % (54) sll $8, $5, 15 # <<15 = ffff8000 %
16 : 00084400; % (58) sll $8, $8, 16 # <<16 = 80000000 %
17 : 00084403; % (5c) sra $8, $8, 16 # >>16 = ffff8000 (arith) %

## Slide 12: Instr. Mem.(3)
18 : 000843c2; % (60) srl $8, $8, 15 # >>15 = 0001ffff (logic) %
19 : 08000019; % (64) finish: j finish # dead loop %
1A : 00000000; % (68) dslot4: nop # DS %
1B : 00004020; % (6c) sum: add $8, $0, $0 # sum function entry %
1C : 8c890000; % (70) loop: lw $9, 0($4) # load data %
1D : 01094020; % (74) add $8, $8, $9 # sum, PIPELINE STALLS %
1E : 20a5ffff; % (78) addi $5, $5, -1 # counter - 1 %
1F : 14a0fffc; % (7c) bne $5, $0, loop # finish? %
20 : 20840004; % (80) dslot5: addi $4, $4, 4 # address + 4, DS %
21 : 03e00008; % (84) jr $ra # return %
22 : 00081000; % (88) dslot6: sll $2, $8, 0 # move result to $v0, DS %

## Slide 13: Data Mem.
0 : BF800000; % 1 01111111 00..0 fp -1 %
14 : 000000A3; % (50) data[0] %
15 : 00000027; % (54) data[1] %
16 : 00000079; % (58) data[2] %
17 : 00000115; % (5C) data[3] %

## Slide 14: Simulation (1)

## Slide 15: Simulation (2)

## Slide 16: Simulation (3)

## Slide 17: Simulation (4)

## Slide 18: Simulation (5)

## Slide 19: Simulation (6)

## Slide 20: Simulation (7)

## Slide 21: Simulation (8)

## Slide 22: Checkpoints
CP 1:
  Waveform Simulation of the Pipelined CPU with the verification program
CP 2:
  FPGA Implementation of the Pipelined CPU with the verification program

## Slide 23
Thanks!